## Slide 1
GSM Signal Denoising and Modulation Classification for Rural Uganda
Final Year Project:
Department of Electrical and Electronics Engineering
Ssemujju Sharif Abdukarim
18/U/ETD/181/GV
Kisige Tom Derrick
22/U/ETD/0953/GV
Supervisor: Dr. Dickson Mugerwa
KYAMBOGO UNIVERSITY
Improving Connectivity in Underserved Areas Using Machine Learning

## Slide 2
Proposal Outline
1
Background
2
Problem Statement
3
Objectives
4
Justification
5
Scope of the Project
6
Literature Review
7
Methodology
8
Tools and Equipment
9
Project Timeline
10
Significance
11
Conclusion
12
References

## Slide 3
Background
UCC reports that network subscriptions reached 33.2 million by the end of 2022, and mobile data traffic doubled from 217 million GB in 2020 to 421.5 million GB in 2022 showing an exponential growth in network service demand. [1]
Unfortunately, network expansion is failing to keep pace with this demand; only 31% of the population and 24% of the landmass have 4G coverage and 62% of the population (30 million people) still lacks mobile internet access, and live in low SNR, high-interference environments where the signal is weak (below -90 dBm), the noise becomes louder than the message, making it impossible for standard tools to understand what is being sent[3][4]
Many people in rural Uganda still use basic phones for calls and Mobile Money, but the signal is often very weak and are being blocked or "noised up" by illegal boosters, unlicensed community radios (Bizindaalo), and heavy tropical rain.

## Slide 4
Background continuation
Automatic Modulation Classification (AMC) is crucial for regulators to monitor the spectrum, manage interference, and identify illegal broadcasters that threaten critical services like aviation.
We propose using a Denoising Autoencoder (DAE) combined with an AMC system that takes a marginal signal (e.g., at -90 dBm or even lower) and actively cleans it up removing noise before trying to classify or demodulate it.
Instead of just trying to read a noisy signal, our system first cleans the signal to make it clear again making sure that even in the most remote sub-counties, the network can still identify and process signals correctly.

## Slide 5
Problem Statement
Many people in rural Uganda still use basic phones for calls and Mobile Money, but the signal is often very weak. When the signal is weak (below -90 dBm), the noise becomes louder than the message, making it impossible for standard tools to understand what is being sent
Other signals are being blocked or noised up by illegal boosters, unlicensed community radios (Bizindaalo), and heavy tropical rain. The Uganda Communications Commission (UCC) finds it hard to catch illegal broadcasters because the current tools cannot see through all this noise. This leads to dropped calls, failed Mobile Money transactions, and poor service for over 30 million Ugandans. Over 70% of call failures in some areas are due to this interference, yet we lack a smart way to clean the signal before processing it.

## Slide 6
Main Objective
Design a Hybrid DAE–AMC Pipeline
To design, implement, and empirically evaluate a hybrid Denoising Autoencoder–Automatic Modulation Classification (DAE–AMC) pipeline that suppresses interference in noisy I/Q streams and maintains accurate modulation decisions across low SNR channel conditions observed in Ugandan networks.

## Slide 7
Specific Objectives
01 - Reasearch
Review AMC and DAE literature emphasizing low SNR mitigation strategies relevant to Ugandan channel conditions.
02 – Design and Implementation
Architect and train Conv1D DAE module reconstructing clean I/Q samples from noisy inputs at −90 dBm thresholds.
Implement supervised AMC classifier ingesting raw and DAE-cleaned signals, quantifying feature preservation.
03 – Evaluation and Testing
Benchmark integrated DAE–AMC against standalone AMC using accuracy, F1-score, confusion matrices across various SNR.

## Slide 8
Justification and Significance
Spectrum Surveillance
It will help with the detection of illegal transmitters and interference mitigation for aviation and public-safety channels.
Rural Broadband
It will help maintains reliable service in low-SNR environments, supporting 30M Ugandans lacking mobile internet access.
Critical Services
Ensures stability for mobile money and e-government services dependent on reliable radio links.
Meeting UCC Mandates: The DAE is explicitly trained on SNR conditions matching UCUSAF's −90 dBm coverage floor, addressing the "near-far" interference documented by UCC QoS audits rather than generic low-SNR scenario
It Aligns with National Policy: Our project supports Uganda's national development plans (NDPIII/NBP) that call for more spectrum-efficient technologies. It replaces older, "brittle" handcrafted methods with a robust, cost effective, software-based AI-based algorithm for enhancing signals by removing noise.

## Slide 9
Scope
Offline Experimentation
Project conducted entirely on a computer using pre-existing data, ensuring a controlled environment.
Public Datasets
DeepSig RadioML 2018.01A benchmark (synthetic, well-characterized SNR labels) and the RF Signal Data collection on Kaggle (real SDR captures providing hardware impairment realism) [11], [12]
Noise Modelling
We inject Uganda-specific noise profiles such as Booster oscillation noise as High-power wideband impulses simulating illegal repeater feedback, Bizindaalo harmonics as Narrowband tones at 2nd/3rd harmonics
of FM frequencies (200 MHz, 300 MHz sidebands leaking into 900 MHz), Rain fade attenuation as Time-varying SNR reduction modeling tropical storm conditions (100+ mm/h rainfall rates)
Model Development
Focus on a Conv1D Denoising Autoencoder (DAE) and a supervised AMC classifier.
Specific Modulations
Training models to recognize GSM-family modulations like GMSK, GFSK, and QPSK
Platform & Tools
Windows OS, Python, TensorFlow, Keras, Jupyter Notebook, and Google Cloud Platform.
Timeline
A 6-month dedicated period for research, model development, and comprehensive testing.

## Slide 10
Literature Review
Chapter Two

## Slide 11
GSM Noise Mitigation in African Networks
While DAE-based signal enhancement has been extensively studied academically, its application to African GSM networks' specific interference environment remains unexplored.
Regulatory Interventions
UCC's enforcement operations confiscate illegal boosters and shut down unlicensed Bizindaalo stations. Proliferation continues due to porous borders and high demand.
Technical Countermeasures
Modern 4G/5G use Massive MIMO and beamforming, but unavailable for legacy 2G/GSM in rural areas. NBI fiber expansion reduces microwave backhaul reliance.
The Research Gap
No published work applies ML-based denoising to UCC-documented GSM interference: booster oscillation, Bizindaalo harmonics, and tropical rain fade.
We fill that gap by training a DAE on synthetic noise profiles matching documented interference vectors, enabling GMSK classification at SNR levels where conventional approaches fail.

## Slide 12
Classical Methods
Early Automatic Modulation Classification (AMC) relied on statistical analysis and manually engineered features. While elegant, these methods are brittle and fail completely in the low-signal, high-interference environments common in Uganda.
Key Limitation:
They are not robust under unknown channels
These impairments are documented by UCC in congested Ugandan deployments motivates the transition toward data-driven feature learning.
Machine learning is the new standard
Modern research has shifted to using deep learning (DL) models like CNNs, Transformers, and Mixture-of-Experts frameworks. These models can learn features directly from raw signal data and have shown significant accuracy improvements, especially in low Signal-to-Noise Ratio (SNR) conditions down to 0 dB.

## Slide 13
Machine Learning in AMC
Deep learning has reshaped AMC by learning discriminative features directly from raw I/Q samples. Recent contributions demonstrate tangible low-SNR gains:
1
AbdElaziz et al. (2023)
Robust CNN with parallel asymmetric kernels achieved 96.5% accuracy at 0 dB and 86.1% at −2 dB across nine modulations.
2
Zhang et al. (2023)
MoE-AMC mixture-of-experts framework yielded ~71.8% averaged accuracy across −20…18 dB—about 10% higher than single-expert models.
3
Meta-Transformer (2024)
Leverages transformer encoders and few-shot learning to adapt rapidly to unseen modulations while maintaining superior accuracy.
4
Rehman et al. (2025)
DLAMC converts I/Q streams into eye diagrams, overcoming the 10–48% accuracy ceiling near −10 dB SNR.
5
Jagannath et al. (2022)
Validated CNN-based multitask AMC on USRP SDR testbed, demonstrating >98% accuracy in live over-the-air experiments.

## Slide 14
Denoising Autoencoders for Signal Enhancement
Denoising frontends have emerged as an effective countermeasure when raw I/Q features are overwhelmed by interference.
75%
Zhang et al.
Dual residual DAE with channel attention improved AMC accuracy by up to 75% across −12…8 dB SNR.
77.5%
DenoMAE
Faysal et al.'s multimodal denoising masked autoencoder sustained 77.5% accuracy at −10 dB—roughly 22% higher without denoising.
70%
Thresholded AE
An and Lee's thresholded autoencoder with SNR predictor delivered ~70% relative accuracy gains on low-SNR samples.
These findings justify the DAE–AMC architecture explored in this project and provide design cues for gating strategies that conserve energy on SDR deployments.

## Slide 15
CHAPTER THREE – METHODOLOGY
A comprehensive framework for developing robust Automatic Modulation Classification systems tailored to challenging RF environments through deep learning and denoising techniques.

## Slide 16
Introduction to Methods
We adopt an experimental research design anchored in reproducible data processing and quantitative benchmarking across four interconnected pillars:
01
Dataset Curation
Aggregate I/Q datasets from simulated and real captures from RF Signal Data and RadioML 2018.01A
02
Controlled SNR Scenarios
Generate SNR conditions (−12 to +18 dB) mimicking edge conditions with added impairments: Rician fading, frequency offsets, and timing jitter.
03
Model Training
Train Conv1D denoising autoencoder (unsupervised) and 1D CNN AMC classifier (supervised) both independently and as integrated pipeline.
04
Comparative Evaluation
Compare hybrid system against standalone baselines using accuracy curves, F1-scores, and confusion matrices for SDR deployment readiness.

## Slide 17
Research Strategy
Dataset Harmonization
Convert datasets to unified tensor format (1024-sample length, normalized amplitude) with stratified train/validation/test splits by modulation and SNR.
Uganda Specific Noise Modeling
Inject three UCC-documented interference types: booster oscillation (wideband impulse), Bizindaalo harmonics (narrowband FM tones), and rain fade attenuation.
DAE Pretraining
Train Conv1D encoder–decoder on noisy/clean pairs using MSE loss until reconstruction PSNR converges, ensuring low-SNR fidelity.
AMC Training
Train baseline on raw GSM-family modulations (GMSK, GFSK, QPSK) inputs, then retrain with DAE outputs to create hybrid pipeline, comparing frozen
and fine-tuned configurations.
Cross-Dataset Evaluation
Assess models on held-out SNR bins, unseen modulation families, and OTA-style splits to expose and quantify domain shift effects.
Deployment Prototyping
Integrate trained models into lightweight inference service with GUI for visualization and regulatory demonstrations.

## Slide 18
Project Budget Overview
The successful execution of this project requires a structured allocation of resources. The total estimated budget is 800,000 UGX, covering critical areas from software to research.
Item
Cost (UGX)
Software Licenses
200,000
Data Curation
100,000
Virtual Machines
200,000
Cloud Databases
100,000
Internet and Research
50,000
Printing and Documentation
50,000
Miscellaneous
100,000
Total Estimated Cost
800,000
This budget ensures that all necessary technical infrastructure, data processing capabilities, and operational requirements are adequately funded to support the project's objectives.

## Slide 19
Project Timeline
Our project will be executed in five distinct phases, ensuring a structured and efficient progression towards our objectives over a 14-week period.
Phase
Description
Weeks
Timeline (Week)
Phase 1: Initiation & Literature Review
Define problem, scope, objectives, and conduct literature review.
1-2
██
Phase 2: Data Acquisition & Preprocessing
Gather datasets, implement preprocessing pipelines, and perform feature extraction.
3-5
███
Phase 3: Model Development & Training
Select & implement ML algorithms, develop models, train & validate.
6-9
████
Phase 4: Testing & Optimization
Evaluate model performance, fine-tune hyperparameters, and optimize.
10-12
███
Phase 5: Documentation & Presentation
Compile research findings, methodologies, results, and prepare presentation.
13-14
██
This timeline ensures a methodical approach to each stage, culminating in a robust and well-documented solution for intelligent signal processing.

## Slide 20
References
[1]: Uganda Communications Commission, “Telephone Subscriptions Rise to 33.2 Million,” UCC Communications Blog, 9 June 2023, https://uccinfoblog.com/2023/06/09/telephone-subscriptions-rise-to-33-2-million/. [2]: Atomic Energy Council, “Radiofrequency Radiation in Uganda,” 2022, https://www.atomiccouncil.go.ug/non-ionizing-radiation-radiofrequency/.
[3] ChimpReports, "Uganda’s Internet users hit 13 million," *ChimpReports News*, Mar. 25, 2024. [Online]. Available: [https://chimpreports.com/ugandas-internet-users-hit-13-million/]
[4] Uganda Communications Commission, "Access Infrastructure Program: Bridging the Digital Divide," UCC Blog, Feb. 2024. [6]: Ghana Chamber of Telecommunications, “Mobile Internet Access Still Limited in Africa, Millions Remain Offline,” citing GSMA data, 2024, https://www.telecomschamber.org/industry-news/mobile-internet-access-still-limited-in-africa-millions-remain-offline/. [7]: Uganda Communications Commission, “UCC cracks down on illegal and non-compliant broadcasters,” 21 October 2024, https://www.ucc.co.ug/ucc-cracks-down-on-illegal-and-non-compliant-broadcasters/. [8]: Xiaolin Zhang et al., “Dual Residual Denoising Autoencoder with Channel Attention Mechanism for Modulation of Signals,” Sensors 23, no. 1023 (2023), https://pmc.ncbi.nlm.nih.gov/articles/PMC9861137/. [9]: Low SNR, Interference & Illegal Transmissions in Uganda’s Wireless Networks, internal research brief, 2025 (synthesizing UCC QoS surveys and enforcement bulletins). [10]: Quantifying the Impact of Low SNR and Interference on Wireless Service Resilience, internal research brief, 2025 (summarizing NDPIII/NBP mandates and AMC accuracy benchmarks). [11]: RF Signal Data, Kaggle, accessed 2025, https://www.kaggle.com/datasets/suraj520/rf-signal-data. [12]: DeepSig Dataset: RadioML 2018.01A, Kaggle, accessed 2025, https://www.kaggle.com/datasets/pinxau1000/radioml2018. [13]: Ramiro Utrilla, “MIGOU-MOD: A dataset of modulated radio signals acquired with MIGOU, a low-power IoT experimental platform,” Mendeley Data V1, 2020, https://data.mendeley.com/datasets/fkwr8mzndr/1. [14]: DeepSig, “RadioML 2016.10A Dataset,” https://www.deepsig.ai/datasets/, accessed 2025. [15]: O. F. Abd-Elaziz, A. M. El-Ghandour, and F. H. Ismail, “Deep Learning-Based Automatic Modulation Classification Using Robust CNN Architecture for Cognitive Radio Networks,” Sensors, vol. 23, no. 23, 2023, Art. 9467, doi:10.3390/s23239467. [16]: J. Gao, Z. Zhang, and Y. Zhang, “MoE-AMC: Enhancing Automatic Modulation Classification Performance Using Mixture-of-Experts,” arXiv preprint, 2023, https://arxiv.org/abs/2312.02298.

## Slide 21
Thanx for Listening