## Slide 1
KYAMBOGO UNIVERSITY
Department of Electrical and Electronics Engineering
Signal Denoising and Intelligent
Modulation Classification
Using Machine Learning
Ssemujju Sharif Abdukarim
18/U/ETD/181/GV
Kisige Tom Derrick
22/U/ETD/0953/GV
Supervisor: Dr. Dickson Mugerwa

## Slide 2
Proposal Outline
Background
Problem Statement
Objectives
Justification & Significance
Scope of the Project
Literature Review
Methodology
Tools and Equipment
Project Budget
Project Timeline
Conclusion
References
Final Year Project Proposal

## Slide 3
Background: Uganda's Mobile Network Challenge
33.2M
Mobile Subscriptions
30M
People Without Internet
31%
4G Coverage Only
Uganda's mobile data traffic has doubled from 217 million GB (2020) to 421.5 million GB (2022), but network expansion cannot keep up.
Rural areas suffer from weak signals and heavy interference from illegal boosters and unlicensed radio stations.
These conditions require advanced technology to clean up noisy signals and identify what type of signal is being transmitted.
Key Insight: UCC needs better tools to monitor the airwaves, catch illegal transmitters, and ensure quality service for all Ugandans.
Source: UCC Communications Report 2022

## Slide 4
Background: Our Proposed Solution
Automatic Modulation Classification (AMC) is how regulators identify signal types. This helps catch illegal transmitters interfering with aviation and other services.
The Problem: When signals are weak and noisy (common in rural Uganda), current AMC systems make many mistakes and cannot identify signals correctly.
Our Solution: We use a Denoising Autoencoder (DAE) - a computer program that learns to clean up noisy signals before identifying them.
How It Helps: By removing noise first, we can correctly identify signals even when very weak (-90 dBm). This improves reliability at network edges.
HOW OUR SYSTEM WORKS
NOISY SIGNAL
↓
DENOISING (DAE)
↓
CLASSIFIER (AMC)
↓
ACCURATE RESULT
DAE-AMC: Denoising Autoencoder + Automatic Modulation Classification

## Slide 5
Problem Statement
Uganda's mobile networks are being pushed to their limits. In rural areas, signals are often too weak (around -90 dBm) and suffer from heavy interference. This makes it difficult for regulators to monitor the airwaves.
PROBLEM 1
Illegal Signal Boosters
Cheap boosters cause massive interference. UCC found 70% of call failures in some areas are from illegal devices.
PROBLEM 2
Unlicensed Broadcasters
Bizindaalo (unlicensed FM stations) use cheap equipment creating interference in mobile frequencies.
PROBLEM 3
Current Tools Fail
Existing classification systems achieve only 72% accuracy in noisy conditions - not enough for reliable monitoring.
The Gap: Without better tools to identify signals in noisy environments, UCC cannot catch illegal transmitters and operators cannot diagnose rural network problems.
Source: UCC Quality of Service Audits, 2019-2024

## Slide 6
Main Objective
OUR GOAL
To design, build, and test a hybrid signal processing system that combines:
Denoising Autoencoder
Cleans noisy signals
+
AMC Classifier
Identifies signal types
Purpose: To accurately identify radio signals even in very noisy, weak-signal conditions found across rural Uganda.
DAE-AMC Pipeline for Low-SNR Environments

## Slide 7
Specific Objectives
Study Existing Research
Review published work on signal classification and noise removal methods that work well in weak signal conditions.
Build the Noise Removal System
Design and train a Denoising Autoencoder that takes dirty, noisy signals and reconstructs clean versions - even when signals are very weak.
Build the Signal Classifier
Create a machine learning classifier that identifies different radio signal types and measure how well cleaned signals preserve important features.
Test and Compare Performance
Compare our combined DAE-AMC system against standard methods using accuracy scores across different noise levels.
Each objective builds upon the previous one to create a complete solution

## Slide 8
Justification and Significance
Meeting UCC Requirements
UCC requires resolving 95% of faults within 24 hours. Impossible when current tools only achieve 72% accuracy.
Supporting National Policy
Aligns with Uganda's National Development Plan (NDPIII) and National Broadband Policy goals.
Spectrum Surveillance
Helps UCC detect illegal transmitters and remove interference affecting aviation and public safety.
Rural Broadband
Maintains reliable service in weak-signal areas, supporting 30 million Ugandans lacking mobile internet.
Critical Services
Ensures stability for Mobile Money and e-Government services millions of Ugandans depend on.
Bottom Line: Our solution replaces old, unreliable methods with intelligent technology that adapts to Uganda's unique interference challenges without needing more radio spectrum.
Supporting NDPIII/NBP directives for spectrum-efficient technologies

## Slide 9
Scope of the Project
Computer-Based Research
All work on computers using existing signal data. No live radio equipment.
Public Datasets
Using RadioML 2018.01A and MIGOU-MOD for training and testing.
Simulated Noise
Adding controlled noise (SNR -12 dB to +18 dB) to mimic real conditions.
Model Development
Building DAE and signal classifier using machine learning.
Signal Types
BPSK, QPSK, 8PSK, 16QAM, 64QAM, AM, and FM signals.
Timeline
14 weeks covering research, development, testing.
PLATFORM AND TOOLS
OS: Windows
Language: Python
Framework: TensorFlow/Keras
Dev: Jupyter Notebook
Cloud: Google Cloud
Controlled laboratory environment using publicly available datasets

## Slide 10
CHAPTER TWO
Literature Review
What researchers have discovered about signal classification and noise removal using machine learning

## Slide 11
The Shift from Old Methods to Machine Learning
CLASSICAL METHODS
The Old Approach
Early signal classification used mathematical formulas and hand-designed rules to analyse signals.
KEY LIMITATION
These methods break down completely when signals are weak or when there is unexpected interference.
MACHINE LEARNING
The New Standard
Modern research uses deep learning - systems that learn patterns directly from signal data, like the brain learns from experience.
KEY ADVANTAGE
These systems can adapt and improve over time, handling different types of interference without reprogramming.
This shift motivates our choice of machine learning for the DAE-AMC system

## Slide 12
What Recent Research Has Achieved
Abd-Elaziz et al. (2023)
96.5%
Accuracy at 0 dB noise using special CNN with parallel filters.
Zhang et al. (2023)
71.8%
Average accuracy using "Mixture of Experts" - 10% better than single models.
Jagannath et al. (2022)
98%+
Real-world tests with actual radio equipment proved lab results transfer.
THE POWER OF DENOISING (Cleaning Signals First)
75%
Improvement with Zhang's DAE
77.5%
Accuracy at -10 dB with DenoMAE
70%
Relative gain with An and Lee
Key Finding: Cleaning the signal before classifying dramatically improves accuracy. This justifies our DAE-AMC approach.
Sources: IEEE Access, Sensors Journal, arXiv preprints (2022-2025)

## Slide 13
CHAPTER THREE
Methodology
How we will build and test the noise-cleaning and signal classification system

## Slide 14
Our Four-Step Research Approach
Gather Data
Collect signal datasets. Add noise to simulate real-world Uganda conditions.
Create Noise
Generate controlled noise (-12 to +18 dB) plus fading and frequency errors.
Train Models
Build and train the DAE and Classifier both separately and together.
Compare
Test DAE-AMC against standard methods. Measure accuracy at each noise level.
RESEARCH APPROACH
Data-Driven Method
We let the computer learn patterns from real signal data rather than programming fixed rules.
Two-Stage Learning
Stage 1: DAE cleans signals. Stage 2: Classifier identifies types. Together they work better.
Experimental research design with reproducible benchmarking

## Slide 15
Research Strategy: Step by Step
Prepare the Data
Convert datasets to same format (1024 samples per signal) and split into training and test sets.
Add Realistic Noise
Inject random noise (AWGN), signal fading, frequency errors, and sudden interference.
Train the Denoiser
Teach DAE to reconstruct clean signals from noisy ones by comparing output to original.
Train the Classifier
First train on raw noisy signals, then retrain using DAE-cleaned signals. Compare both.
Test Across Conditions
Evaluate at different noise levels matching UCUSAF coverage conditions (-90 to -60 dBm).
Build Demo System
Create simple interface showing before/after cleaning and classification results.
HOW WE MEASURE SUCCESS
Accuracy: How often correct
F1-Score: Balance of precision/recall
Confusion Matrix: Error patterns
SNR Curves: Performance vs noise

## Slide 16
Project Budget
Item
Cost (UGX)
Software Licenses
200,000
Data Curation
100,000
Virtual Machines (Cloud)
200,000
Cloud Databases
100,000
Internet and Research
50,000
Printing and Documentation
50,000
Miscellaneous
100,000
TOTAL
800,000
TOTAL BUDGET
800,000
Uganda Shillings
Budget Notes
Most work uses free software (Python, TensorFlow)
Cloud computing needed for ML training
No hardware purchase - all computer-based
Budget covers all technical infrastructure and operational requirements

## Slide 17
Project Timeline: 14 Weeks
Phase 1: Planning
Weeks 1-2
Define scope; Literature review
Phase 2: Data Prep
Weeks 3-5
Gather and process datasets
Phase 3: Model Building
Weeks 6-9
Build DAE and AMC models
Phase 4: Testing
Weeks 10-12
Evaluate and fine-tune
Phase 5: Documentation
Weeks 13-14
Write report; Present
14
Total Weeks
5
Phases
4
Weeks Building
3
Weeks Testing
Structured approach ensuring thorough research, development, and documentation

## Slide 18
Conclusion
THE PROBLEM
Rural Uganda suffers from weak mobile signals and heavy interference. Current monitoring tools fail in noisy conditions, achieving only about 72% accuracy.
OUR SOLUTION
A two-stage system that first cleans noisy signals (DAE), then identifies signal types (AMC). Research shows this approach can improve accuracy by up to 75%.
Better Monitoring
Help UCC catch illegal transmitters even in noisy conditions
Rural Coverage
Support network expansion to underserved communities
National Goals
Align with NDPIII and National Broadband Policy objectives
A practical, software-based solution for Uganda's spectrum management challenges

## Slide 19
References
[1] Uganda Communications Commission, "Telephone Subscriptions Rise to 33.2 Million," UCC Blog, June 2023.
[2] Ghana Chamber of Telecommunications, "Mobile Internet Access Still Limited in Africa," citing GSMA data, 2024.
[3] Uganda Communications Commission, "UCC cracks down on illegal broadcasters," October 2024.
[4] X. Zhang et al., "Dual Residual Denoising Autoencoder with Channel Attention for Signals," Sensors 23, 2023.
[5] RF Signal Data, Kaggle, 2025. https://www.kaggle.com/datasets/suraj520/rf-signal-data
[6] DeepSig Dataset: RadioML 2018.01A, Kaggle, 2025. https://www.kaggle.com/datasets/pinxau1000/radioml2018
[7] R. Utrilla, "MIGOU-MOD: A dataset of modulated radio signals," Mendeley Data, 2020.
[8] O. F. Abd-Elaziz et al., "Deep Learning-Based AMC Using Robust CNN," Sensors, vol. 23, 2023.
[9] J. Gao et al., "MoE-AMC: Enhancing AMC Using Mixture-of-Experts," arXiv preprint, 2023.
[10] A. Jagannath, "Multi-Task Learning for Modulation Classification for 5G," Physical Communication, 2022.
[11] M. Faysal et al., "DenoMAE: A Multimodal Autoencoder for Denoising Signals," arXiv preprint, 2025.
[12] H. An and B.-M. Lee, "Robust AMC in Low Signal-to-Noise Ratio," IEEE Access, vol. 11, 2023.
Full reference list available in the written proposal document

## Slide 20
Thank You
For Your Attention
We welcome your questions and feedback
Ssemujju Sharif Abdukarim
18/U/ETD/181/GV
Kisige Tom Derrick
22/U/ETD/0953/GV
Department of Electrical and Electronics Engineering
KYAMBOGO UNIVERSITY