## Slide 1
Project title
Final Year Project | 1
GSM Signal Denoising and Modulation Classification for Rural Uganda
Final Year Project Presentation
Department of Electrical and Electronics Engineering
Kyambogo University
Ssemujju Sharif Abdukarim | 18/U/ETD/181/GV
Kisige Tom Derrick | 22/U/ETD/0953/GV
Supervisor: Dr. Dickson Mugerwa

## Slide 2
Introduction / Background
Final Year Project | 2
BACKGROUND
Rural mobile service is often present, but still too weak to depend on
Local service reality
• Basic GSM services still matter: voice, SMS, USSD, and Mobile Money.
• At the cell edge, a phone may show signal bars but still suffer noisy or unstable service.
• Weak I/Q structure makes reliable modulation interpretation difficult under low SNR.
Engineering interpretation
• The project treats weak service as a signal-quality problem, not only a coverage-map problem.
• Denoising is placed before classification so the AMC stage sees a cleaner signal representation.
• The same logic can support troubleshooting, spectrum monitoring, and rural service planning.
GSM-family I/Q
Working signal model
Baseband windows test noisy edge-of-coverage conditions.
DAE + AMC
Core technical pipeline
Denoising front end followed by automatic modulation classification.
Rural use case
Project motivation
Weak-signal interpretation can support practical network decisions.

## Slide 3
Problem statement
Final Year Project | 3
WHAT THE PROJECT ADDRESSES
Problem statement
Rural GSM users may experience unreliable service even where a network signal is visible. At the edge of coverage, received I/Q samples are degraded by low SNR, interference, fading, and unstable propagation. Conventional AMC methods can misclassify such noisy signals, making it harder to interpret the real service condition.
Technical gap
• Classical signal-processing filters are useful, but are usually fixed to known noise assumptions.
• Deep-learning AMC can classify raw I/Q samples, but low-SNR interference still reduces reliability.
• A denoising front end may recover useful signal structure before classification.
Project question
• Can denoising improve modulation classification under controlled low-SNR GSM-family conditions?
• Which SNR ranges benefit most from denoising-assisted classification?
• How should the results be interpreted for rural weak-service analysis?

## Slide 4
Objectives
Final Year Project | 4
MAIN AND SPECIFIC OBJECTIVES
Aim and objectives
Main objective: design and evaluate a denoising-assisted automatic modulation classification pipeline for noisy GSM-family I/Q signals in rural Uganda weak-service scenarios.
Specific objectives
• Define GSM-family low-SNR and interference scenarios for controlled evaluation.
• Design a denoising front end that reconstructs cleaner I/Q representations.
• Train and evaluate an AMC stage on raw noisy and denoised signal features.
• Compare baseline and denoising-assisted performance using accuracy, macro F1, confusion behavior, and signal plots.
• Interpret the findings for weak-service troubleshooting and rural connectivity planning.

## Slide 5
Justification, significance, and scope
Final Year Project | 5
JUSTIFICATION AND SCOPE
Why this project matters
Justification
• Rural weak service is a practical problem for ordinary users and for network planning.
• Denoising before classification gives a measurable way to test whether useful signal structure can be recovered.
• The method is software-side and can be evaluated without transmitting or interfering with licensed networks.
Significance
• Supports better interpretation of noisy edge-of-coverage signals.
• Gives supervisors and reviewers visible before/after signal evidence.
• Creates a foundation for future Android/SDR receive-only prototype work.
Scope
• Controlled simulation and offline I/Q evaluation.
• GSM-family/proxy modulation classes used for AMC validation.
• No claim of completed field deployment or live service improvement.
Receive-only
Safety boundary
The project does not transmit into licensed spectrum.
Offline first
Evaluation boundary
The current results are controlled simulation outputs.
Prototype path
Next step
Android/SDR demonstration remains a future validation pathway.

## Slide 6
Literature review
Final Year Project | 6
EVIDENCE BASE
Literature review: where the gap sits
Classical AMC
• Uses likelihood rules, moments, cyclostationary features, and engineered descriptors.
• Can be interpretable, but becomes fragile when assumptions about noise and channel conditions break.
• Useful as a baseline for explaining what the ML pipeline improves.
Deep-learning AMC
• Learns discriminative patterns directly from raw or transformed I/Q samples.
• Modern CNN and sequence models perform well when trained on representative SNR conditions.
• Performance still drops when signal structure is buried under low-SNR and interference.
Denoising front ends
• Denoising autoencoders and related methods reconstruct cleaner signals before downstream tasks.
• The key research question is not only whether the signal looks cleaner, but whether classification improves.
• This project evaluates denoising as a preprocessing block for AMC under weak-service conditions.
Gap: few student-level implementations connect denoising, AMC metrics, and rural GSM weak-service interpretation in one reproducible pipeline.
Sources: ProjectReport.md literature review; DeepSig/RadioML datasets; low-SNR AMC and denoising references captured in reports/.

## Slide 7
Methodology
Final Year Project | 7
SYSTEM DESIGN
Methodology: denoising-assisted AMC signal chain
1
I/Q source
Synthetic GSM-family or public I/Q windows.
→
2
Impairment
Low SNR, narrowband interference, fading, phase/frequency offset.
→
3
Denoising
Reconstruct cleaner signal representation before classification.
→
4
AMC
Classify modulation from raw/noisy or denoised features.
→
5
Metrics
Accuracy, macro F1, confusion matrix, and signal plots.
Evaluation comparison
• Baseline path: noisy I/Q features -> AMC classifier.
• Denoising-assisted path: impaired I/Q -> denoising front end -> AMC classifier.
• Both paths are evaluated under the same SNR levels and classes.
• This makes the difference attributable to the denoising front end.

## Slide 8
Preliminary controlled simulation setup
Final Year Project | 8
RESULTS BASIS
Preliminary controlled simulation setup
4
Modulation classes
GMSK-like, QPSK, 8PSK, and 16QAM.
4
SNR levels
-8, -4, 0, and 4 dB controlled impairment settings.
1,920
Test windows
240 held-out windows per SNR and pipeline comparison.
20260524
Random seed
The run is deterministic and reproducible.
What was simulated
• Baseband I/Q windows with GSM-family/proxy modulation structure.
• Low-SNR AWGN, narrowband interference, mild fading, and phase/frequency offset.
• A denoising-assisted path compared against a noisy baseline path.
What was not claimed
• No field capture result is claimed in this slide deck.
• No live call, SMS, USSD, or Mobile Money improvement is claimed.
• No physical tower range extension is claimed.

## Slide 9
Preliminary results
Final Year Project | 9
CONTROLLED SIMULATION
Preliminary result: denoising makes weak signal structure easier to inspect
Noisy, denoised, and clean reference waveform comparison
Constellation comparison at a low-SNR operating point
Interpretation: the preliminary denoising stage is not presented as final DAE performance. It is a controlled signal-processing validation layer that shows why denoising before AMC is worth completing.

## Slide 10
Preliminary results
Final Year Project | 10
CONTROLLED SIMULATION
Preliminary result: denoising-assisted AMC improves low-SNR classification
Accuracy by SNR: noisy baseline versus denoising-assisted AMC
49.4%
Noisy baseline
Mean accuracy across controlled SNR levels.
52.0%
Denoising-assisted
Mean accuracy with the denoising-assisted path.
+9.2 pts
Largest observed gain
At 0 dB in this preliminary controlled run.
Result status: preliminary controlled simulation, not final field validation.

## Slide 11
Discussion of results
Final Year Project | 11
INTERPRETATION
Discussion: what the preliminary results mean
Denoising-assisted confusion matrix across controlled SNR levels
Observed pattern
• The denoising-assisted path improves the controlled run overall.
• The clearest gain appears around the difficult 0 dB condition.
• Cleaner SNR conditions do not require aggressive denoising, so adaptive bypass is sensible.
Limitations
• The samples are synthetic and should be replaced or supplemented with stronger datasets.
• The denoising block is preliminary; final DAE training remains the next technical step.
• The results do not prove live service improvement or physical coverage extension.

## Slide 12
Conclusion and recommendations
Final Year Project | 12
FINAL POSITION
Conclusion and recommendations
Conclusion
• Weak rural GSM service can be studied through noisy I/Q signal interpretation, not only through coverage-map labels.
• The proposed DAE-AMC chain is technically coherent: denoise first, classify second, evaluate across SNR.
• Preliminary controlled simulation results support continuing the denoising-assisted AMC implementation.
Recommendations
• Complete the full trained DAE and AMC implementation with stronger dataset coverage.
• Report results by SNR band using accuracy, macro F1, confusion matrices, and signal-quality plots.
• Use receive-only validation only; do not transmit, decode private content, or claim live-service gains without evidence.
Next 4 weeks
Implementation focus
DAE training, AMC benchmarking, final report update, and presentation rehearsal.
Final output
Expected deliverable
A reproducible denoising-assisted AMC evaluation for weak GSM-family signals.
Safety
Operating boundary
Receive-only, offline-first validation unless formal approval changes the scope.

## Slide 13
References
Final Year Project | 13
SOURCES USED
References and artifact provenance
Selected references
• Uganda Communications Commission reports and service-quality materials referenced in ProjectReport.md.
• DeepSig / RadioML I/Q dataset literature for AMC evaluation framing.
• Low-SNR AMC and denoising-autoencoder papers summarized in reports/LowSNR_AMC_Denoising_Research.md.
• Project report manuscript: ProjectReport.md, final-year project workspace.
Preliminary simulation provenance
• Script: reports/preliminary_simulation_2026_05_24/run_preliminary_dae_amc.py
• Metrics: reports/preliminary_simulation_2026_05_24/results.csv
• Figures: signal_comparison.png, constellation_comparison.png, accuracy_by_snr.png, confusion_denoised.png
• Status: controlled simulation artifacts generated for presentation submission, not field deployment evidence.
Thank you.